Physics 37100 Advanced Physics Laboratory I

Lab #3

(PART I:  Single measurements)

- Create a sketch to measure the light output of a PWM LED using pin 9.

  - Use the brightest LED with corresponding series resistor from previous Lab.  Set the brightness of the LED to 128 using analogWrite.

  - Use the photoresistor in series with a resistor to measure the light output on A0.  It might be useful to put the LED and photoresitor into a tube to eliminate outside light.

    - What resistance did you use? Why?

  - Output the value of A0 to the serial port every 1/10 of a second for 10 seconds.

- Repeat for brightness 0, 64, and 255, and using digitalWrite HIGH in place of analogWrite.

- Analyze the data.

  - Copy and paste the data from the serial monitor.

  - Import to Matlab or other data analysis program.

  - Find and report the mean and standard deviation (STD) for each of the 5 brightnesses.

    - Which has the largest STD? Why?

    - Is there a difference between analogWrite of 255 and digitalWrite of HIGH? Explain.

    - Is 128 twice as bright as 64? Explain.

(PART II:  Time resolved measurements)

- Modify your sketch to measure the light output of a PWM LED over time using pin 9.

  - Create a 512 element unsigned int array Vs to hold the time series data.

  - Acquire the data in a for loop with n running 0-511. Only use Vs[n]=analogRead(inPin) inside the loop so that we can get the data as fast as possible.

  - Time the loop by saving the value of micros() just before and just after the loop.

  - After the loop output all of the array values and the time of the loop to the serial port.

  - Do all of the work in setup() so that you do not fill up your serial monitor

- Analyze the data.

  - Copy and paste the data in the serial monitor to matlab or other plotting program.

  - Assume that each acquisition took equal time and use the total time to find the time for each point.  Is this a good assumption? Explain.

  - Plot the data versus time for analogWrite values of 0, 128, 255, and for digitalWrite value of HIGH.  How does this help explain the data from 3c above?