Physics 37100 Advanced Physics Laboratory I

Lab #4

(PART I:  Wait for it…)

- Create a sketch that waits for the letter ‘?’ over the serial port.  When it receives ‘?’ it will send back ‘K’ and turn on and LED.

  - Set a poll time of 200 μs using delayMicroseconds() to check Serial.available().

  - Use Serial.read() to examine each character that is sent.  If the character is not ‘?’ then continue to wait.

  - Test the sketch using the serial monitor.

- Convert the sketch into a function waitFor().

  - waitFor should take 3 inputs:

    - A character to wait for.

    - A poll time, which should default to 200 μs.

    - A time out period, which should default to 60e6 μs.

  - waitFor should output true if it reads the character and false if the time out period expires.

  - Rewrite and test the sketch from 1) using your new function waitFor(‘R’).

    - Try waiting for other characters.

    - Test the defaults and overrides.

- Make a Matlab script that sends the character ‘?’ over the serial port.

  - using code similar to this:

s=serial('COM8');  % Create serial object

fopen(s);          % Open serial port

pause(2);          % Wait for port to open

fprintf(s,’?’);    % Send character ‘?’

%% Always close -- use: fclose(instrfind);delete(instrfind) %  to close orphans

fclose(s);

delete(s);

clear s;

  - Test to make sure the LED only lights when ‘?’ is sent.

- Add code to the matlab script to wait for the character ‘K’ to be sent over the using fgetl() (type “doc serial/fgetl” for info).

- Using the code developed above we have a way to establish communications between matlab and the arduino.  It is like a short conversation: matlab asks ‘?’ == ‘Are you ready?’ and arduino responds ‘K’ == ‘Yes, I am OK.’.

  - Save the sketch and matlab script to send with your report.