Physics 37100 Advanced Physics Laboratory I

Lab #4

(PART II:  Simple oscilloscope)

- Using the code and circuit from part I and lab 3-II, create a sketch to:

  - establish communication with matlab using ‘?’ and ‘K’;

  - wait to receive the character ‘g’ (for go);

  - make one loop to take 512 points of time series data from photoresistor on A0 measuring the PWM pin 9 LED set to 128;

  - make a second loop to send the data to matlab using Serial.println();

  - at the end of the second loop send the total acquisition time;

  - loop back to part b.

- Modify (part I) matlab script to:

  - establish communication with arduino using ‘?’ and ‘K’;

  - send the character ‘g’ (for go);

  - loop over the serial data using fgetl() and str2double() to store the data in an array;

V=zeros(1,N);

t=(0:N-1)/N;

for m=1:N

str=fgetl(s);

V(m)=str2double(str);

end

  - read the acquisition time using fgetl() and str2double();

  - plot the data using a time axis in μs;

  - drawnow;

  - Loop back to part b.

- Move the wire connected to A0 to other points in the circuit while the script is running to see the data update.

- Change the plotting to display the FFT of the data.

  - The horizontal axis should be in Hz.  Include a nice plot of the FFT with x and y axis labels in the report.

  - What is the frequency of the PWM light?

  - Is it consistent with the value in the description of analogWrite on the arduino site: https://www.arduino.cc/en/Reference/AnalogWrite.

  - Measure the frequency directly using the time series data to measure the time from one peak to the next.  Is it consistent?

- (Extra credit) modify to allow matlab to set the value of the LED output on each loop.